## Slide 1: Mid-Project Reviews
Indoor Drone
Group 9

## Slide 2: Project Stages
Finish soldering electrical parts
Created a simulated environment
Basic function commands
Assembled Drone components
Unit testing
Progress

## Slide 3
Drone version 1
It is hard to access the firmware to adjust the code inside and debug
Because this type of board usually using for racing or entertainment purpose, we could not find any support resources. So, it is hard for us to modify the FC.
It is small so it’s very difficult for us soldering things together
Not supported for stage 2 (autopilot controlling)
Cons
Widely used.
Firmware is supported with Betaflight (open source platform)
Can connect with camera for further usages
Having video transmitter feature
Small and light, suitable for small drone
Pros
Matek F405-mini

## Slide 4
Drone version 2
Automated
Support customization and better automation capability
Semi-automated
Drone
A new controller that fits our requirements
New flight controller
With what we’ve learned and available resources
Drone v1.0

## Slide 5
Require external hardware to connect to the internet
Only one USB port to connect to computer
Low memory prone to froze when executing codes
Arduino is only suitable for performing repetitive, simple tasks.
Cons
ARDUINO
controller
Low cost
On board storage
Pros

## Slide 6
NAVIO2 flight controller + Raspberry pi model 3B
RPi
Raspberry Pi is a general-purpose computer
More suitable to control complicated machine like robots
Capable of doing intense calculations
Capable of performing multiple complicated tasks
Wi-Fi capable
NAVIO2
Run on Linux environment
Easy to setup and interact with
Can SSH into your drone while its flying
Can update firmware wirelessly ( with Wi-Fi )
PROS

## Slide 7
NAVIO2 flight controller + Raspberry pi model 3B
RPi
Expensive
Difficult to power using battery pack
Require SD card for storage
Risk of files corruption and software problems
NAVIO2
Is not optimize for real time application
May experience hiccup when run resource heavy scripts
Very new and not widely seen in industrial applications
CONS

## Slide 8
Decision made
F450 frame
Transfer drone component to smaller frame after finished drone v2
Frame
Smaller frame
New platform
Using Ardupilot and Dronekit as platform to support coding to control the drone through a companion computer
Connection method
First phrase will be control the drone by using ssh
GPS tracking
Using Nogps to guide the drone flight to a direction, an alternative ways instead of using GPS
Arduino
Change from using Arduino as alternative plan to Raspberry pi + Navio 2
Platform
Stages
Stages
Changes
Raspberry pi + Navio 2
Ardupilot + Dronekit
SSH
nonGPS navigation

## Slide 9
Hardware challenges
Get a modern PowerPoint Presentation that is beautifully designed. I hope and I believe that this Template will your Time.
Repurpose firmware
Some parameters, stored in ardupilot-raspberry, are not suitable when working with indoor-environment.
Problem by problem
We are still working to solve this problem by searching this error, trying to adjust the value of parameters relating to Pre-arm Safety Checks
Manual flight mode
Drone does not arm even if we change the manual flight modes that do not require GPS for the purpose of indoor flight
Pre-arm check
Configuring the settings of Pre-arm Safety Checks in Mission Planner (a ground control station for Plane, Copter and Rover)
Failsafe triggers
The pre-arm check and the imported parameters does not fit and triggers failsafe error

## Slide 10
Autonomous status
Ardupilot is open source autopilot software
ArduPilot
Capable of controlling almost any vehicle system imaginable
ArduPilot
Has advanced data-logging, analysis and simulation tools.
ArduPilot
API allows developers to create Python apps that communicate with vehicles over MAVLink
Dronekit
A best solution to our indoor copter that uses onboard companion computers with the addition of open source library
Dronekit

## Slide 11
Drone diagram

## Slide 12
SITL simulator
(Software in the loop)
Directly on your computer
Without any special hardware
Simulated data
The SITL (software in the loop) simulator allows you to run Plane, Copter or Rover without any hardware. It is a build of the autopilot code using an ordinary C++ compiler, giving you a native executable that allows you to test the behavior of the code without hardware.

## Slide 13
Software challenges
Flight mode
Navigation
Communication
Communication
Bug happens when we try to use guided flight mode script
Guided mode flight code
nonGPS flight script is still in researching
nonGPS navigation
Bugs and errors when implementing scripts onto drone
Script integration
Connection code between drone and ground control station is still unstable. Vary between computers and network state
Connection between drone and station

## Slide 14
Team member contribution
Drone Version 1:
Research frames and drone schematics
Research components (propeller, ESC, FC, PDB, motor, battery)
Solder drone parts:
    Solder wires to drone controller (FC)
    Solder ESC to FC
Install firmware to drone controller
Install Flight controller software(Beta-flight) to laptop
Connect flight controller to laptop and configure drone settings
Adjust radio control signals
Test motors and RX signals (receiver)
Test indoor flight
Hoan (Hardware)
Drone version 2:
Research compatible drone-hardware
Find suitable ground control
Assemble drone parts (Raspberry Pi, Navio2, ESC…) to drone frame
Solder ESCs and drone power distribution board to test motor
Install raspbian and ardupilot firmware to RPi
Configure ardupilot in RPi
SSH to RPi via wifi
Install mission planner (ground control station) on laptop and configure/connect to RPi on drone
Test ground connection with hardware
Calibrate ESC and compass of drone with mission planner
Adjust parameters of ardupilot in Rpi to let the drone arm

## Slide 15
Team member contribution
Drone Version 1:
Research frames and drone schematics
Research components (propeller, ESC, FC, PDB, motor, battery)
Assemble drone components:
  Attach components to the frame
  Attach propeller with motors
Install firmware to drone controller:
Install Flight controller software(Beta-flight) to laptop
Connect flight controller to laptop and configure drone settings
Calibrate ESCs and propellers
Test motors and RX signals (receiver)
Thịnh (Hardware)
Drone version 2:
Research compatible drone-hardware
Assemble drone parts (Raspberry Pi (Ppi), Navio2, ESC…) to drone frame
Solder ESCs and drone power distribution board to test motor
Install raspbian and ardupilot firmware to Rpi
Configure ardupilot in Rpi
SSH to Rpi via wifi
Install mission planner (ground control station) on laptop and configure/connect to Rpi on drone
Test ground connection with hardware
Calibrate ESC and compass of drone with mission planner

## Slide 16
Team member contribution
Research compatible platform (software)
Configuration detecting plugin fly control board for betaflight
Drone component research
Research on drone frame and model
Buying drone component
Config Matek f405mini firmware from betaflight
Basic drone movement script (take-off, landing, configuration, velocity setting)
Simple go-to script (Flight forward)
nonGPS navigating solutions (Manually import flight path)
Guided flight script (drone take-off, move forward and landing without using GPS)
Huy (Software)

## Slide 17
Team member contribution
Research compatible platform (software)
Configuration flashing port to connect the board
Drone component research
Research on drone frame and model
Fixing Transmitter can’t activate armed mode to control
Establish component into drone frame
Set up simulated environment
Parameter configuration
Basic drone movement script (connection)
Connecting APM planner to script to simulate script
Establish connection between companion computer to raspberry pi
Y (Software)

## Slide 18
Team member contribution
Test run simulator
Start SITL (Software in the Loop) drone
Documentation
Hardware compatibility test
Config Drone version 1
  Fix calibrations
  Fix telemetry connection
Quan (Tester)

## Slide 19
Future plan
Solve hardware problems
Establish connection between companion computer with copter
Apply mission plan into copter
Optical-flow research to increase safety while flying

## Slide 20: Thank you